## Slide 1: Viewing in 3D
In 2D, we specify
a window on the 2D world and
a viewport on the 2D view surface.
Objects in the world are clipped against the window and are then transformed into the viewport for display.
In 3D, we specify
a view volume in the world,
a projection onto a projection plane, and
a viewport on the view surface.
Objects in the 3D world are clipped against the 3D view volume and are then projected. The contents of the projection of the view volume onto the projection plan, called the window, are then transformed into the viewport for display.

## Slide 2: Viewing in 3D
Viewing requires three basic elements
  One or more objects
  A viewer with a projection surface
  Projectors that go from the object(s) to the projection surface
Classical views are based on the relationship among these elements
  The viewer picks up the object and orients it how she would like to see it
Each object is assumed to constructed from flat principal faces
  Buildings, polyhedra, manufactured objects

## Slide 3
Clip against
view volume
3D world-coordinate
output primitives
Clipped
world
coordinates
2D device
coordinates
Project onto
projection
plane
Transform into
viewport in 2D
device coordinates
for display

## Slide 4: Planar Geometric Projections
Standard projections project onto a plane
Projectors are lines that either
  converge at a center of projection
  are parallel
Such projections preserve lines
  but not necessarily angles
Nonplanar projections are needed for applications such as map construction

## Slide 5: Perspective vs Parallel
Computer graphics treats all projections the same and implements them with a single pipeline
Classical viewing developed different techniques for drawing each type of projection
Fundamental distinction is between parallel and perspective viewing even though mathematically parallel viewing is the limit of perspective viewing

## Slide 6: Perspective Projection
Projectors coverage at center of projection

## Slide 7: Perspective Projection

## Slide 8: Parallel Projection

## Slide 9: Computer Viewing
There are three aspects of the viewing process, all of which are implemented in the pipeline,
  Positioning the camera
    Setting the model-view matrix
  Selecting a lens
    Setting the projection matrix
  Clipping
    Setting the view volume

## Slide 10: Computer Viewing
3D viewing involves not just a projection, but also a view volume against which the 3D world is clipped.
The projection and view volume together provide all the information needed to clip and project into 2D space.
view angle

## Slide 11
The windows have a certain aspect ratio
view angle
Points lying inside the view volume are projected onto the viewplane.
OpenGL clips off any parts of the scene that lie outside the view
volume.

## Slide 12: Setting the view volume
The shape of the camera’s view volume is encoded in the projection matrix.
glMatrixMode(GL_PROJECTION);//make the projection matrix current
glLoadIdentity(); // start with a unit matrix
gluPerspective(viewAngle, aspectRatio, N,F); //load the appropriate value

## Slide 13: The OpenGL Camera
In OpenGL, initially the world and camera frames are the same
  Default model-view matrix is an identity
The camera is located at origin and points in the negative z direction
OpenGL also specifies a default view volume that is a cube with sides of length 2 centered at the origin
  Default projection matrix is an identity

## Slide 14: Default Projection
Default projection is orthogonal
clipped out
z=0
2

## Slide 15: Moving the Camera Frame
If we want to visualize object with both positive and negative z values we can either
  Move the camera in the positive z direction
    Translate the camera frame
  Move the objects in the negative z direction
    Translate the world frame
Both of these views are equivalent and are determined by the model-view matrix
  Want a translation (glTranslatef(0.0,0.0,-d);)
  d > 0

## Slide 16: Moving Camera back from Origin
default frames
frames after translation by –d
d > 0

## Slide 17: Moving the Camera
We can move the camera to any desired position by a sequence of rotations and translations
Example: side view
  Rotate the camera
  Move it away from origin
  Model-view matrix C = TR

## Slide 18: OpenGL code
glMatrixMode(GL_MODELVIEW)
glLoadIdentity();
glTranslatef(0.0, 0.0, -d);
glRotatef(90.0, 0.0, 1.0, 0.0);

## Slide 19: The LookAt Function
The GLU library contains the function glLookAt to from the required modelview matrix through a simple interface
Note the need for setting an up direction
Still need to initialize
  Can concatenate with modeling transformations
Example: isometric view of cube aligned with axes
glMatrixMode(GL_MODELVIEW):
glLoadIdentity();
gluLookAt(1.0, 1.0, 1.0, 0.0, 0.0, 0.0, 0., 1.0. 0.0);

## Slide 20
gluLookAt(eye.x, eye.y, eye.z, look.x, look.y, look.z, up.x, up.y, up.z)

## Slide 21
It is useful to attach a coordinate system to the camera.
This coordinate system has its origin at the eye, and has three axes, u,
v, and n

## Slide 22: Other Viewing APIs
The LookAt function is only one possible API for positioning the camera
Others include
  View reference point, view plane normal, view up (PHIGS, GKS-3D)
  Yaw, pitch, roll
  Elevation, azimuth, twist
  Direction angles

## Slide 24
What are the directions of u,v, and n when we execute gluLookAt()?
n = eye – look
u = up x n
v = n x u

## Slide 25
The transformation that gluLookAt() sets up
The gluLookAt() sets up the transformation matrix V that converts
world coordinates to camera coordinates and the matrix M that
embodies all of the modeling all of the modeling transformations
applied to points.

## Slide 26: Projections and Normalization
The default projection in the eye (camera) frame is orthogonal
For points within the default view volume
Most graphics systems use view normalization
  All other views are converted to the default view by transformations that determine the projection matrix
  Allows use of the same pipeline for all views
xp = x
yp = y
zp = 0

## Slide 27: Perspective Projections of 3D objects

## Slide 28: Perspective projection of a point
Note that the denominator term is larger for more remote points .
This introduces perspective forshortening and makes remote parts of an object appear smaller than nearer parts.

## Slide 29
Straight lines project to straight lines.

## Slide 30
Example:

## Slide 31
View 1: Set the camera’s eye at (0,0,2) and have it look down the
negative z-axis, with u = (1,0,0), n = (-1,0,0)
Set the near plane at a distance of unity from the eye.
All points on the front wall have Pz = -1
All points on the back wall have Pz = -2
Any point (Px,Py,Pz) on the front wall projects to P’= (Px,Py)
Any point on the back wall projects to P’= (Px/2,Py /2)

## Slide 32
View 2: Set the camera’s eye at (0.5,0,2) , u and n are the same.
Set the near plane at a distance of unity from the eye.

## Slide 33
View 3: Set the camera’s eye at (2,5,2) , look = (0,0,0).

## Slide 34
Perspective Projection of a line
Suppose a line in 3D passes through the point A = (Ax, Ay, Az) and
the direction vector c = (cx,cy,cz).
P(t) = A + ct.
Suppose the line A + ct is parallel to the viewplane. Then cz = 0
This is the parametric form of a line with slope cy/cx

## Slide 35
If two lines in 3D are parallel to each other and to the viewplane, they
project to two parallel lines.
All parallel lines share the same vanishing point. In particular, they
project to lines that are not parallel.

## Slide 36
A grid of lines

## Slide 37
Adding Pseudodepth
Taking a projection discards information on depth; we lose information
about how far a point is from the eye.

## Slide 38
Adding Pseudodepth
The actual distance of a point P from the eye, is
Cumbersome and slow to compute

## Slide 39
What is a good choice for the pseudodepth function?
We will choose a and b s.t. the pseudodepth varies between -1 and 1.

## Slide 41: Homogeneous Coordinate Form
Recall that a point P=(Px,Py,Pz) has the representation
(Px,Py,Pz,1) in homogeneous coordinates and
a vector v=(vx,vy,vz) has the representation (vx,vy,vz,0)
Now we extend the idea and say that a point P=(Px,Py,Pz) has a whole family of homogeneous representations
(wPx,wPy,wPz,w) for any value of w except 0.
e.g. the point (1,2,3) has representations (1,2,3,1), (2,4,6,2), (.3,.6,.9,.3)

## Slide 42: Homogeneous Coordinate Form
Consider and affine transform
q = Mp where
M =

## Slide 43
What if we deviate from a fourth row of (0,0,0,1)?
consider

## Slide 44
Which point is this?
Dividing through the fourth component
Perspective transformation!!
Perspective division!!

## Slide 45
Perspective projection
Perspective projection = perspective transformation + orthographic
projection

## Slide 46
Transforming the view volume
The perspective transformation “warps” objects so that, when viewed with an orthographic projection, they appear the same as the original objects do when viewed with a perspective projection

## Slide 47
Transforming the view volume

## Slide 48
OpenGL composes the perspective transformation with another
mapping that scales and shifts this parallelepiped into the canonical
view volume, a cube that extends from -1 to 1 in each dimension.

## Slide 49
Two steps
  Move center to origin
    T(-(left+right)/2, -(bottom+top)/2)
  Scale to have sides of length 2
    S(2/(left-right),2/(top-bottom),2/(near-far))
R =
This is the projection matrix, and it performs the perspective
transformation plus scaling and shifting to transform the camera’s view
volume into the canonical view volume.

## Slide 50
R =
This is the matrix, that OpenGL creates (and by which it multiplies the
current matrix) when glFrustum(left,right,bott,top,N,F)
is executed.

## Slide 51
The view volume bounds the portion of the scene that is to be clipped
out and projected onto the view plane. However, the view volume
depends on the type of projection.

## Slide 53
Canonical View Volume
The canonical view volumes are a prism for parallel projections
and the truncated right regular pyramid for perspective projections.
It is much easier to clip to these volumes than to an arbitrary view
volume, so view volumes are often transformed to one of these before
clipping.

## Slide 54
Clipping Faces against View Volume
A point lies inside the camera’s view volume if its transformed version
lies inside the canonical view volume.

## Slide 55
Back-face culling can be performed to eliminate the polygons which
are facing away from the viewer.
Culling is a process where any polygon facing away from the view
direction is labeled as 'invisible' and ignored through the rest of the
pipeline.

## Slide 57
The test for visibility is quite straightforward and is best carried out in
view space.
We calculate the outward normal for a polygon and apply it to the
following equation:
If Np . N > 0 then the polygon is visible, otherwise invisible where:
Np is the polygon normal N is the vector from the polygon to the
viewpoint ('line of sight' vector)

## Slide 58
The Cohen-Sutherland algorithm (3D Version)
The Cohen-Sutherland algorithm extends to 3D very simply.
The outcode for 3D clipping is a 6-bit code. For a parallel canonical
view volume the bits represent:
bit 1 - point above view volume (Y>1)
bit 2 - point below view volume (Y<-1)
bit 3 - point to the right of view volume (X>1)
bit 4 - point to the left of view volume (X<-1)
bit 5 - point behind view volume (Z<-1)
bit 6 - point in front of view volume (Z>0)

## Slide 59
As in the 2D case, the line may be trivially accepted
(both outcodes=000000), or trivially rejected
((code 1 AND code 2) not 000000).
Otherwise line subdivision is used again. The points of intersection
with the clipping edges are found using a parametric representation of
the line being clipped.

## Slide 60
View the CVV as six infinite planes and consider where the given
edge lies relative to each plane in turn.
Suppose we want to clip the line segment AC against the CVV.

## Slide 61
A +(C-A)t
If A and C lie on the same side of a wall, no need to compute the
intersection of the edge with the wall.
If A and C lie on opposite sides, locate the intersection point and clip
off the part of the edge that lies outside the wall.

## Slide 62
We need to test whether a point is on the “outside” or “inside” of a plane.
Consider the plane x = -1. The point A lies to the right of it
(on the “inside) if

## Slide 64
Following the clipping operation, perspective division is finally done.

## Slide 65: Pipeline View

## Slide 66: OpenGL Orthogonal Viewing
glOrtho(xmin,xmax,ymin,ymax,near,far)
glOrtho(left,right,bottom,top,near,far)
near and far measured from camera

## Slide 67: OpenGL Perspective
glFrustum(xmin,xmax,ymin,ymax,near,far)

## Slide 68: Using Field of View
With glFrustum it is often difficult to get the desired view
gluPerpective(fovy, aspect, near, far) often provides a better interface
aspect = w/h
front plane

## Slide 69: Notes
We stay in four-dimensional homogeneous coordinates through both the modelview and projection transformations
  Both these transformations are nonsingular
  Default to identity matrices (orthogonal view)
Normalization lets us clip against simple cube regardless of type of projection
Delay final projection until end
  Important for hidden-surface removal to retain depth information as long as possible

## Slide 70: Final Projection
Set z =0
Equivalent to the homogeneous coordinate transformation
Hence, general orthogonal projection in 4D is
Morth =
P = MorthST

## Slide 71: Producing Stereo Views
To make a stereo view, two pictures – a “left eye” and a “right eye” picture – are made using slightly different cameras.
The cameras have the same LookAt point, but different eye positions.

## Slide 72
Where do we put the left and right eye?

## Slide 73: Taxonomy of Planar Geometric Projections
parallel
perspective
axonometric
multiview
orthographic
oblique
isometric
dimetric
trimetric
2 point
1 point
3 point
planar geometric projections

## Slide 74: Vanishing Points
Parallel lines (not parallel to the projection plan) on the object converge at a single point in the projection (the vanishing point)
Drawing simple perspectives by hand uses these vanishing point(s)
vanishing point

## Slide 75
Perspective projections are categorized by their number of principal vanishing points and therefore by the number of axes the projection plane cuts.
One point perspective views

## Slide 76: One-Point Perspective
One principal face parallel to projection plane
One vanishing point for cube

## Slide 77: Two-Point Perspective
On principal direction parallel to projection plane
Two vanishing points for cube

## Slide 78
The infinite grid in two-point perspective

## Slide 79: Three-Point Perspective
No principal face parallel to projection plane
Three vanishing points for cube

## Slide 80
Escher’s Ascending and Descending: a three-point perspective.

## Slide 81: Advantages and Disadvantages
Objects further from viewer are projected smaller than the same sized objects closer to the viewer (diminuition)
  Looks realistic
Equal distances along a line are not projected into equal distances (non-uniform foreshortening)
Angles preserved only in planes parallel to the projection plane
More difficult to construct by hand than parallel projections (but not more difficult by computer)

## Slide 82
Parallel Projections
To what point p does P project?

## Slide 83
Using n=(0,0,1), and project onto the xy plane for which B=(0,0,0)

## Slide 84
Parallel Projections
Oblique Orthographic
Oblique = the projection direction d is not parallel to n
Orthographic = the projection direction d is parallel to n

## Slide 85: Orthographic Projection
Projectors are orthogonal to projection surface
In orthographic projections, dx and dy are zero.

## Slide 86: Orthogonal Normalization
glOrtho(left,right,bottom,top,near,far)
normalization  find transformation to convert
specified clipping volume to default

## Slide 87: Orthogonal Matrix
Two steps
  Move center to origin
    T(-(left+right)/2, -(bottom+top)/2,(near+far)/2))
  Scale to have sides of length 2
    S(2/(left-right),2/(top-bottom),2/(near-far))
P = ST =

## Slide 88: Multiview Orthographic Projection
Projection plane parallel to principal face
Usually form front, top, side views
isometric (not multiview
orthographic view)
front
side
top
in CAD and architecture,
we often display three
multiviews plus isometric

## Slide 90: Advantages and Disadvantages
Preserves both distances and angles
  Shapes preserved
  Can be used for measurements
    Building plans
    Manuals
Cannot see what object really looks like because many surfaces hidden from view
  Often we add the isometric

## Slide 91: Axonometric Orthographic Projections
Allow projection planes that are not normal to a principle axis and therefore show several faces of an object at once.
classify by how many angles of
a corner of a projected cube are
the same
none: trimetric
two: dimetric
three: isometric
q 1
q 3
q 2

## Slide 92: Axonometric Orthographic Projections
foreshortening

## Slide 93: Types of Axonometric Projections
All 3 principle axes foreshortened equally.
All 3 principle axes foreshortened unequally.
2 principle axes foreshortened equally.

## Slide 94: Advantages and Disadvantages
Lines are scaled (foreshortened) but can find scaling factors (all three principal axes are equally foreshortened
Lines preserved but angles are not
  Projection of a circle in a plane not parallel to the projection plane is an ellipse
Can see three principal faces of a box-like object
Some optical illusions possible
  Parallel lines appear to diverge
Does not look real because far objects are scaled the same as near objects
Used in CAD applications

## Slide 95: Oblique Projection
Orthographic projections preserve the exact shape of one face of an object, but do not reveal its 3D nature very well.
Axonometric projections show a 3D quality, but do not yield the
exact shape of any of the faces of the object.
Oblique projections are an attempt to combine the uesful properties of
both orthographic and axonometric projections.
They usually present the exact shape of one face of an object (the most
important face), while simultaneously revealing the general 3D
appearance of the object.

## Slide 96: Oblique Projections
Oblique Projection = Shear + Orthogonal Projection

## Slide 97: Oblique Projection
Arbitrary relationship between projectors and projection plane

## Slide 99: Advantages and Disadvantages
Can pick the angles to emphasize a particular face
  Architecture: plan oblique, elevation oblique
Angles in faces parallel to projection plane are preserved while we can still see “around” side
In physical world, cannot create with simple camera; possible with bellows camera or special lens (architectural)

## Slide 100: Classical Projections

## Slide 101: OpenGL Perspective
glFrustum allows for an unsymmetric viewing frustum (although gluPerspective does not)

## Slide 102: OpenGL Perspective Matrix
The normalization in glFrustum requires an initial shear to form a right viewing pyramid, followed by a scaling to get the normalized perspective volume. Finally, the perspective matrix results in needing only a final orthogonal transformation
P = NSH
our previously defined
perspective matrix
shear and scale

## Slide 103: Why do we do it this way?
Normalization allows for a single pipeline for both perspective and orthogonal viewing
We keep in four dimensional homogeneous coordinates as long as possible to retain three-dimensional information needed for hidden-surface removal and shading
We simplify clipping